2.12 Version of BLAST (Last version 2.14)
Older version	New version	Description	Default	Type
-a (number of cpu or threads)	-num_threads	Specifies the number of processor threads to use	single thread	integer
-C (checkpoint directory)	-checkpoint_interval	Interval between PSI-BLAST checkpoint saves		integer
-d (database)	-db	Specify the database to search against		filename
-d (multiple databases)	-subject	Use multiple subject databases in the search
-D
-e (E-value threshold)	-evalue	E-value threshold for saving hits		integer
-g (perform gapped alignment)	-ungapped (For ungapped alignment. Omit this flag for gapped.)	Determines whether the search performs gapped alignment	N/A	flag
-E	-gapextend	Cost assigned for each symbol (nucleotide or amino acid) inserted into an existing gap	2	integer
-G	-gapopen	Cost assigned when an alignment introduces a new gap	5	integer
-F (low-complexity filtering)	-dust	turns on/off low-complexity filtering for nucleotide sequences	yes or no	string
-hspmax	-max_hsps	Set the maximum number of HSPs (High-Scoring Pairs) retained for each alignment.	0 (blastn, blastp, blastx)	integer
-i (input file)	-query	Input file containing query sequences		filename
-I (pseudocount constant)	-pseudo_const	Pseudocount constant used in PSI-BLAST
-J (pseudocount exponent)	-inclusion_ethresh	E-value threshold for including sequences in PSI-BLAST		integer
-K (keep PSI-BLAST checkpoint)	-checkpoint	Enable checkpointing for PSI-BLAST runs		filename
-L (pseudocount low)	-query_loc	range of the query sequence to search against the database		range
-l (GenInfo Identifier)	-show_gis	Includes NCBI GIs in the output	N/A	flag
-o	-outfile	Output format options		filename

-M (matrix)	-matrix	Specifies the scoring matrix to use	BLOSUM62	string
-m (output format)	-outfmt	Output format to store the results	0 (pairwise format) / 6 (tabular format) / 7 (tab format with comments) / 11 (asn.1 binary) / 15 (json)	integer
-S	-strand	The search strand	3	integer
-T	-html	Produce HTML format output
-U	-lcase_masking	lowercase masking	n/a	flag if True
-v (number of database sequences)	-max_target_seqs	Limits the number of returned matches	500 (blastn, blastp, blastx, tblastn) / 1000 (PSI-BLAST)	integer
-W (word size)	-word_size	Word size for initial matches	11	integer
-X	-xdrop_gap	X-dropoff value for gapped alignment extension	20	float
-y	-xdrop_ungap	X dropoff value for ungapped extensions in bits	30	float
-Y (effective search space)	-searchsp	Sets the effective search space (for calculation of E-values)		integer
-z (effective database size)	-dbsize	Sets the effective database size (for calculation of E-values)		integer
-Z	-xdrop_gap_final	X dropoff value for final gapped alignment in bits	100	float
bl2seq	blastn, blastx, tblastx, tblastn, blastp	Compares two sequences (nucleotide or protein) using BLAST and reports local alignments.
blastall	blastn, blastx, tblastx, tblastn, blastp	Separate executables for different types of BLAST searches
blastgp	psiblast	Position-Specific Iterated BLAST (PSI-BLAST) is used to perform iterative searches for homologous sequences and build a position-specific scoring matrix. It is particularly useful for detecting distant homologs.
blastn	megablast	Compares a nucleotide query sequence against a nucleotide sequence database using BLAST.
fastacmd	blastdbcmd	Extracts sequences from a BLAST database based on sequence identifiers or coordinates.
formatdb	makeblastdb, blastdb_aliastool	Creates a BLAST database from a FASTA file containing sequences.
rpsblast	rpstblastn	Reverse Position-Specific BLAST for translated nucleotide queries (RPSTBLASTN) searches a translated nucleotide query against a protein database using a position-specific scoring matrix (PSSM). This is commonly used to detect distant protein homologs.

BLASTN protocol
page 131

legacy:
blastall -p blastn -d <genome> -i >oligo> -G 2 -E 1 -F F

blast+:
blastn -db <genome> -query <oligo> -gapopen 2 -gapextend 1 -dust no

legacy:
megablast -d <genome> -i <oligo> -W 11 -F F -D 2

add
-task megablast

page 133

legacy:
blastall -p blastn -d <genome> -i <dna> -G 1 -E 3 -W 30 -F “m D” -U -e 1e-20

blast+:
blastn -db <genome> -query <oligo> -gapopen 1 -gapextend 2 -word_size 30 -dust yes -soft_masking true -lcase_masking -evalue 1e-20
/*
Gap existence and extension values 1 and 4 are not supported for substitution scores 1 and -2
2 and 2 are supported existence and extension values
1 and 2 are supported existence and extension values
0 and 2 are supported existence and extension values
3 and 1 are supported existence and extension values
2 and 1 are supported existence and extension values
1 and 1 are supported existence and extension values
2 and 2 are supported existence and extension values
Any values more stringent than 2 and 2 are supported
*/

page 134

legacy:
blastall -p blastn -d <genome> -i <cDNA> -G 1 -E 3 -W 15 -F "m D" -U -e le-20

blast+ command:
blastn -db <genome> -query <oligo> -gapopen 1 -gapextend 2 -word_size 15 -dust yes -soft_masking true -lcase_masking -evalue 1e-20

blast+ example:
blastn -db rchiobhm_db/RchiOBHm-V2.0-20170227.fna -query fragaria_vesca_orf.fa -gapopen 1 -gapextend 2 -word_size 15 -dust yes -soft_masking true -lcase_masking -evalue 1e-20

legacy:
megablast -d <genome> -i <cDNA> -W 12 -F "m D" -U -t 21 -N 0 -D 2

blast+:
add
blastn -db <genome> -query <oligo> -word_size 12 -dust yes -soft_masking true -lcase_masking [-t 21] [-N 0] -task megablast

page 135

legacy:
blastall -p blastn -d <genome> -i <dna> -r 1 -q -1 -G 1 -E 2 -W 9 -F “m D” -U

blast+
blastn -db <genome> -query <dna> -reward 1 -penalty -1 -gapopen 1 -gapextend 2 -word_size 9 -dust yes -soft_masking true -lcase_masking

page 137

legacy :
blastall -p blastn -d <est_db> -i <genome> -r 1 -q -1 -G 1 -E 2 -W 9 -F “m D” -U -e 1e-20 -b 100000 -v 100000

blast+
blastn -db <genome> -query <dna> -reward 1 -penalty -1 -gapopen 1 -gapextend 2 -word_size 9 -dust yes -soft_masking true -lcase_masking -num_alignments 100000 -num_descriptions 100000

page 140

legacy :
blastall -p blastn -d <db> -i <est> -G 1 -E 3 -W 30 -U -v 10000 -b 10000 -e 1e-10

blast+ :